## Slide 1: Unit 2 Numerical Representations
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Today’s Lecture
How do we represent numeric values in a finite numbers of bits?
More generally, how can values be compressed?
What representations are computationally simple?
What representations result in good approximations to reality?
The world is continuous and infinite, but computers are finite

## Slide 3: Example 1: Embedded LLMs
Full LLMs require massive amounts of memory
  Cannot work on embedded devices
Quantization
  Aggressive reduction in number of bits / parameter
  Ex: INT4 vs. FP32
New techniques have enabled very low footprint
  Often 1 to 1.5 GB
Performance often remains excellent
  With judicious choice of approximation techniques
Kurtic, Eldar, et al. "“Give Me BF16 or Give Me Death”? Accuracy-Performance Trade-Offs in LLM Quantization." Proceedings of the 63rd Annual Meeting of the Association for Computational Linguistics (Volume 1: Long Papers). 2025.

## Slide 4: Example 2: Next-Generation Wireless
Massive MIMO systems in cellular base stations
  100s – 1000s of antennas
  Each antenna gets data at ~1 Gsamp/s
Data rate and processing is overwhelming
Very low-rate quantization has been key
  2- 4 bits per antenna
Uplink performance vs number of quantization levels
Jacobsson, S., Durisi, G., Coldrey, M., Gustavsson, U., & Studer, C. (2017). Throughput analysis of massive MIMO uplink with low-resolution ADCs. IEEE Transactions on Wireless Communications, 16(6), 4038-4051.

## Slide 5: Compression Research at NYU
ML techniques at the forefront for learning new compression
NYU has several leading researchers in the area
Ballé, J., Laparra, V., & Simoncelli, E. P. (2016). End-to-end optimized image compression. arXiv preprint arXiv:1611.01704.
Jona Balle, NYU

## Slide 6: Learning Objectives
Represent numbers in various formats: Integers, floating point, fixed point
Implement arithmetic operations efficiently in these format
Identify cases for overflow
Evaluate approximation errors via simulation
Optimally select scaling factors and parameters for the formats
Convert floating point algorithms to fixed point

## Slide 7: Outline
Integers, Truncation, and Overflows
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of FixP Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 8: Integers
We will use notation
  : Signed integer with bits in two complement
  : Unsigned integer with bits
Range:
Example: With bits
  Range of
  Range of

## Slide 9: Truncation
Occurs when a variable is assigned a value out of range
In above code we need
When is outside this range, SystemVerilog will truncate:
  Take the LSBs of
  Sign extend if necessary
Equivalent to

## Slide 10: Sample Problem
Can see problem on LLM auto grader

## Slide 11: Solution using Binary Representations

## Slide 12: Solution using Modulo Arithmetic

## Slide 13: Simulating Truncation in Python
This code works for numpy arrays
Mask the LSB
Then sign extend if necessary

## Slide 14: Saturation
Truncation results in values far different from original
  Ex: Truncate to 4 signed bits
Alternatively, can saturate
  Clip to max or min values before assignment
  Ex: Truncate 9 to 7
  Provides less approximation error
  But adds a bit of extra logic
Example to right:
  Want to assign

## Slide 15: Addition Overflow Rules
Consider adding
If and are both signed or both unsigned:
  No overflow requires
  bit width of
If is signed and is unsigned,
  No overflow requires
  Example if (4 bits signed), (4 bits unsigned)
  Sum is which needs 6 bits signed.

## Slide 16: Sample Problem
See solution in the autograder

## Slide 17: Addition with Truncation
Given a potential overflow, SV will:
  Create a temporary variable with no overflow
  Temporary variable has enough bits
  Then it will truncate to lower bits
Saturation must be implemented manually

## Slide 18: Multiplication Overflow
Consider multiplying
  and may be signed or unsigned
To prevent overflow, we need:
With overflow:
  SV implements truncation

## Slide 19: Summary
Two integer types: = signed integers = unsigned
Each has finite range
Assignments outside that range result in overflow
In case of overflow, system Verilog performs truncation
Optionally, you can add code to explicitly saturate
  Offers better performance but adds additional logic
Arithmetic operations result in bitwidth growth
  Addition of 2 numbers requires 1 extra bit
  Multiplication of 2 numbers requires width = product of the two numbers

## Slide 20: Outline
Integers, Truncation, and Overflows
Floating Point Numbers
Fixed Point Numbers
Mapping Floating to Fixed Point in Python
System Verilog Implementation

## Slide 21: Limitations of Integers
Consider integers or
Cannot handle fractional components
  Ex: 7.9, -12.2
  Rounding may cause excessive approximation error
Limited range
  Values overflow for and for

## Slide 22: Simple Floating Point
Fixed point
Signed bit:
  1, One bit
Exponent, bits
Mantissa, significand, bits
  Unsigned integer. Not two complement
  is the precision
Fixed scale factor
  Constant, no bits
  Used to set range of
  More later
1
Bits=
bits total

## Slide 23: Example
Consider some values with:
  Precision Exponent width =
  Scale
  These values are never used. Just for demo
Total number of bits = bits
Mantissa range is Exponent range
Table to the right shows values with

## Slide 24: Example Problem

## Slide 25: Solution

## Slide 26: Terminology
To compare ways of representing numbers, we introduce some terminology
Class or Format: A finite set of real-valued numbers
  Example:
Bit representation: The bit encoding used to store each element in the class:
  For integer: Representation is the two-complement or unsigned integer
  For FP: representation is the triple
Decoded or numeric value: The real-value for a given bit representation
  Example:

## Slide 27: Dynamic Range
A benefit of Floating point is its dynamic range
Dynamic range: Given a number class:
  Represents span between the max before overflow and underflow
Often quoted in dB:
Or bits:

## Slide 28: Dynamic Range of Integers
Consider signed bit integers:
Max value:
Min non-zero value:
Hence dynamic range of integers:
For integers, dynamic range is:
  equal to number of non-sign bits

## Slide 29: Floating-Point Dynamic Range
Recall:
Largest value for :
Smallest non-zero value for
Dynamic range:
For floating point:
  Grows exponentially with

## Slide 30: Example Comparison
32-bit integer:
  Range goes from 1 to
  Dynamic range in linear scale
  bits
32-bit floating point:
  Dynamic range in bits: bits
  Dynamic range in linear scale
FP has orders of magnitude more range

## Slide 31: IEEE-754 Floating Point Standard
Format | Mantissa bits (stored) | Significand precision (with implicit 1) | Exponent bits
FP16 (half) | 10 | 11 | 5
FP32 (single) | 23 | 24 | 8
FP64 (double) | 52 | 53 | 11

## Slide 32: IEEE 754 Normal and Sub-Normal
For FP32: precision and exponent width
Uses a two regions
Normal region:
  Exponent in range
  In this region:
  The is as if the has an implicit leading bit of
  Note that
Sub-normal region:
  Exponent
  In this region:
  Used for small numbers

## Slide 33: IEEE 754 Properties
Single precision (FP32):
  Largest normal
  Smallest normal
  Smallest sub-normal
  Vastly greater range than 32-bit integers
Double precision (FP64):
  Largest normal
  Smallest normal
  Smallest sub-normal

## Slide 34: Floating Point Addition
Consider two numbers in normal region (sub-normal performed similarly)
We need the representation for the sum:
WLOG: Assume For simplicity assume: (other cases are similar)
Then:
Value
Since we need for normal numbers, we shift
If set otherwise
Take

## Slide 35: Resulting Algorithm
Given two numbers: with
Compute
If set
Else
Set
Handle overflow and underflow
Then:
Conclusion: We can perform addition of two FP numbers
But requires considerable extra logic for multiple cases and overflow / underflow

## Slide 36: Floating Point Multiplication
Consider two numbers in normal region (sub-normal performed similarly)
We need the representation for the product:
WLOG: Assume
Then: where (XOR) and
We need If :
  and
Handle overflow and underflow
Can perform multiplication, but requires considerable extra control logic

## Slide 37: Comparison
Integer 32 32-bit multiplier
  Implementation requires just the product: 64-bit result
FP32 FP32 multiplier
  Significand multiply: 24×24 → 48‑bit product (including hidden bit).
  Exponent path: add exponents, subtract bias, detect overflow/underflow.
  Normalization: possible shift + exponent adjust.
  Rounding: guard/round/sticky bits, increment logic, possible renormalization.
  Special cases: zeros, subnormals, infinities, NaNs, sign rules.
FP multiplication typically takes 2 to 4 complexity

## Slide 38: Outline
Integers, Truncation, and Overflows
Floating Point Numbers
Fixed Point Numbers
Mapping Floating to Fixed Point in Python
System Verilog Implementation

## Slide 39: Motivating In-Class Exercise
Try the following jupyter notebook

## Slide 40: Integers vs. Floating Point
Integers:
  Pro: Easy arithmetic. No extra bits for exponent
  Cons: Do not natively handle fractional components.
  Cons: Limited dynamic range
Floating point:
  Pro: Large dynamic range, handles fractional components
  Cons: Arithmetic is harder, some loss of precision to store exponent
Is there a way to handle fractions without increased computation overhead?

## Slide 41: Fixed Point
Floating point: use a mantissa and exponent:
  Both mantissa and exponent are variables
  Gives large dynamic range, but makes arithmetic more complex
Fixed point: Key idea: Fix the exponent
  is a standard integer with bits
  Scale factor is fixed, not variable. Does not need to be stored or manipulated
  Allows fractional values.

## Slide 42: Fixed Point Q Notation
and : Standard fixed-point representation
  : number of integer bits
  : number of fractional bits
  = signed values, : unsigned values
Each element is simply a integer,
  is called the integer representation
Corresponds to a real-valued number:

## Slide 43: Examples
Take
Find closest approximation with:
  and varies
Table shows:
  value (qbits): integer representation
  Floating point value:
We see as increases:
  More accurate representation

## Slide 44: Properties
Suppose that or Type equation here.
Total number of bits
Range:
Resolution: Minimum positive number:
Dynamic range:
  : bits
  : bits

## Slide 45: Arithmetic Operations
Suppose that and are bit representations of and
  Assume they are the same parameters and for now
Addition:
  with
  Addition of numeric values = Addition of the integer representations
Multiplication:
  with
  Multiplication of the numerical values = multiplication of integer values with
Same overflow rules as integers

## Slide 46: Example Problem

## Slide 47: Solution

## Slide 48: Type Casting
Suppose that in the bit representation in .
We want to convert to
Since where
Implementable with left shift by or right shift by
For will overflow when
Overflow can only occur when :
  Why? Suppose
  Since No overflow
However changing or may change precision

## Slide 49: Comparison
Property | 32-bit integer | 32-bit floating point FP32 | 
Complexity | Easy | Moderately hard | Easy
Can handle fractional values | No | Yes | Yes
Dynamic range | Low | High | Low
Property |  | 32-bit floating point FP32 | 
Complexity | Easy | Moderately hard | Easy
Can handle fractional values | No | Yes | Yes
Dynamic range | Low | High | Low

## Slide 50: Outline
Integers, Truncation, and Overflows
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of FixP Numbers
Converting Floating Point Algorithms to Fixed Point

## Slide 51: Selecting the Precision
Suppose we have a real-valued number
Want to represent as in
How do we select and ?
Total width determined by storage and complexity
For a fixed width we can vary
How do we select ?

## Slide 52: Probabilistic Analysis
Let variable to quantize
Model as a random variable
  The HW will see different values over time
Example to right:
  Blue = PDF of
  Fixed = total bitwidth
  Red lines = Qunatization bins for
Selecting
  Tradeoff of overflow and precision
Minimal overflow Low precision
High overflow High precision
More integer bits
More fractional bits

## Slide 53: Encoding, Representation, and Decoding
Analyze any number class with three components: Encode, representation, decoding
For fixed-point, we use the notation:
  : Encodes a real number to an integer representation
  : Decodes an integer representation back to a real number
Real value
Decode
Encode
Quantized
Real value
Representation
Ex:

## Slide 54: Mean Squared Error
Consider some encoding and decoding:
  and
Suppose that real value can be modeled probabilistically
  Has a probability density function
Then we can measure the mean squared error:
  Measures the average error
  Includes error to both precision and overflow
We can then select to minimize MSE
Assumes we have a PDF of
  That is, we know what values we are expecting

## Slide 55: Optimal Selection of
Example to the left:
For each we try different
Initially MSE decreases with
  Higher precision
But then MSE increases
  Overflow
Optimal value is a few bits below

## Slide 56: Outline
Integers, Truncation, and Overflows
Floating Point Numbers
Fixed Point Numbers
Optimal Scaling of Fix Point Numbers
Converting Floating Point Algorithms to Fixed Point